1. To kill the theft alarm on the 93-94 models, cut the Violet/Yellow wire at pin 4 of the theft alarm module. Ground the cut wire on the module side. Have the keys out of the ignition and all doors and hood closed when grounding the wire. This will disarm the theft alarm system and prevent the theft alarm from arming.

2. Another way is to disconnect the theft alarm module once the system is disarmed, either by grounding the Violet/Yellow wire or unlocking the vehicle using the key in one of the front doors or lift gate.