Problem Set II 	Soil Water

- Gravitational potential is determined by the height of the points above the reference level.

- Capillary or matric potential must be measured and, therefore, is provided.

- Total potential energy is simply the sum of the component potentials.

- Water flows from higher energy to lower energy.

- The Gradient is determined by the difference in total energy between the two points divided by the distance between the points.

- Multiplying the gradient by the hydraulic conductivity yields the total flow.

1. Soil water potentials:

100 cm

75 cm

50 cm

25 cm

0 cm							reference

Note the soil diagram above. Point A is at 75 cm; point B is at 25 cm above the reference.

The capillary potential energy at point A is -100 cm.

The capillary potential energy at point B is -200 cm.

What is the total potential energy at point A? ___ -100 cm + 75 cm = -25 cm ___

What is the total potential energy at point B? _____ -200 cm + 25 cm = -175 cm ___

Will water flow between the points? _____ Yes ___________________________

If so, in what direction? ____ From point A to point B _________

What is the gradient between the two points? ____ (-25 – (-175)) / (75 – 25) = ___ 3 _______

If K = 10 cm/hr, determine the flow, Q between the points. __ (10 cm/hr)(3) = 30 cm/hr __

2. Soil Water potential:

400 cm

300 cm

200 cm

Reference

100 cm

Note the soil diagram above. Point A is at 300 cm; point B is at 100 cm.

The capillary potential energy at point A is -400 cm.

The capillary potential energy at point B is -300 cm.

Note the reference level on the Figure

What is the gravitational potential energy at point B? ____ 0 _________

What is the height of point A above the reference level? ____ 200 cm _____

What is the gravitational potential energy at point A? ___ 200 cm ________

What is the total potential energy at point A? ___ -400 + 200 = -200 cm ____

What is the total potential energy at point B? ______ -300 cm + 0 = -300 ________

Will water flow between the points? _____ Yes _______________________

If so, in what direction? _____ From point A to point B _____

What is the gradient between the two points? _ (-200 – (-300) / (300 – 100) = 0.5 ____

If K = 5 cm/hr, determine the flow, Q between the points. _ (5 cm/hr)(0.5) = 2.5 cm/hr

3. Soil Water potential:

400 cm

Reference

300 cm

200 cm

100 cm

10 cm	 20 cm

Note the soil diagram above. Points A and B are at 300 cm.

The capillary potential energy at point A is -200 cm

The capillary potential energy at point B is -100 cm.

Note the reference level for gravitational Potential.

Will water flow between the points? ________ Yes ____________________1pt

If so, in what direction? __ From point B to point A _______________1pt

What is the difference in total potential energy between the points? _ -100 – (-200) = 100 cm _ 1pt

What is the gradient between the two points?____(100 cm) / (20 – 10) = 10 ___________ 2pts

If K = 10 cm/hr, determine the flow, Q between the points. _(10 cm/hr)(10) = 100 cm/hr _ 2 pts

# Text boxes

A

B

A

B

A

B