Name:____________________________

CMIS 310 – Summer 2016

HOMEWORK #6 – Week #6

This homework is worth 10% of your course grade.

Read each problem carefully.  Failure to follow the instructions for a problem will result in a zero score for that problem.

Submit the completed Homework via Assignment in LEO.

- A 32-bit computer has two selector channels and one multiplexor channel. Each selector channel supports two magnetic disk and two magnetic tape units.  The multiplexor channel has two line printers, two card readers, and ten VDTs terminals connected to it.  Assume the following transfer rates.

Disk drive	800 Kbytes/s

Magnetic tape drive	200 Kbytes/s

Line printer	6.6 Kbytes/s

Card Reader	1.2 Kbytes/s

VDT	1 Kbytes/s

Estimate the maximum aggregate I/O transfer rate in this system.

2.        Given the following set of events, show which routines the CPU is executing for times 0 to 100 ns.  Each handler routine (with its interrupt request) takes 20 ns to complete.  The priority of the interrupts ranges from IRQ6 as the highest priority interrupt to IRQ0 as the lowest priority interrupt.

| Time | Action |
| --- | --- |
| 0 ns | Start of main program |
| 10 ns | IRQ1 |
| 20 ns | IRQ3 |
| 35 ns | IRQ4 |
| 50 ns | IRQ6 |

Time		Action

0 ns:		Start of Main Program

- s:		IRQ1

- If an address bus needs to be able to address sixteen devices, how many conductors will be required? What if each of those devices also needs to be able to talk back to the I/O control device?

- Define the terms seek time, rotational delay, and transfer time. Explain their relationship.

- Suppose a disk drive has the following characteristics:

- 6 surfaces

- 1024 tracks per surface

- 128 sectors per track

- 512 bytes/sector

- Track-to-track seek time of 10 milliseconds

- Rotational speed of 6000 RPM.

- What is the capacity of the drive?

- What is the access time?

.