Country:United States

Make:gmc

Model:Sierra 1500 HD Pickup

Year:1992

Engine:5.7

Customer

i have replaced every electrical component on my 1992 gmc pickup to stop shuddering when i drive up a steep hill. ihave paid for some and performed some of the replacements after receiving good advice. the 5.7 runs perfectly but today i had to drive up a fairly steep highway about 60 mph and i topped the hill at 30 mph violently shuddering to the top and then it smoothed out

14 Jun 2016, 6:38 PM

Customer

i also installed a new fuel pump, new fuel injectors, new fuel regulator, new muffler ,new tires, new timming gear, new timming chain, hi temperature liquid sensor, map sensor, new fuel filter

14 Jun 2016, 7:29 PM

Me

I wonder if this has a lock-up torque convertor and that is giving you a problem.

Is this an automatic transmission?

14 Jun 2016, 7:39 PM

Customer

yes

14 Jun 2016, 7:40 PM

Me

Ok, is this the C1500 2WD or K1500 4WD?

14 Jun 2016, 8:03 PM

Customer

k1500 4wd

14 Jun 2016, 8:05 PM

Customer

mileage is 445,000 mi

14 Jun 2016, 8:06 PM

Me

yeah, I see in 3rd-D4 the torque convertor clutch is applied.

14 Jun 2016, 8:07 PM

Me

I am reading that the torque convertor should be locked up in 3rd or 4th gear when the speed is above 24 mph and several other things, but first to determine if it is even the torque convertor lockup that is even causing the problem. I suppose the easiest way to check is to just disconnect the TCC for now. Test drive it and see if it still shudders.

Let me see if I can find a fuse to pull or something, give me a minute or two.

14 Jun 2016, 8:11 PM

Me

Yes, the gage fuse, remove it and see if it still shudders, if not, then we can start diagnosing that tcc circuit, cause I just read the "4th gear signal to ECM. This signal will not prevent TCC engagement, but could cause a change in engage/disengage speed points."

14 Jun 2016, 8:13 PM

Customer

thank you mike . tomorrow i will try your suggestions.

is there a way i can print these statements

terry

14 Jun 2016, 8:23 PM