| 2002 Dodge or Ram Truck RAM 1500 Truck 2WD V8-5.9L VIN Z | Save Article | Top of Form Bottom of Form |
| --- | --- | --- |

Zoom and Print Options Tests 1 - 4 Zoom and Print Options Tests 5 - 9 Zoom and Print Options Test 10 SYMPTOM P0132-1/1 O2 SENSOR SHORTED TO VOLTAGE WHEN MONITORED With battery voltage greater than 10.4 volts, engine running for more than 4 minutes and coolant temperature above 180 °F. SET CONDITION The oxygen sensor voltage is above 1.5 volts. POSSIBLE CAUSES - O2 sensor operation - O2 sensor signal shorted to voltage - O2 sensor signal circuit shorted to ASD relay output (O2 heater supply circuit) - O2 sensor signal open - O2 sensor ground circuit open - O2S heater supply circuit open - O2 sensor heater ground circuit open - Intermittent condition - PCM