| 1. | Disconnect and isolate the negative battery cable. |
| --- | --- |

| 2. | If equipped, remove the floor console, (Refer to 23 - Body/Interior/CONSOLE, Floor - Removal) . |
| --- | --- |

| 3. | Remove the cup holder if equipped, (Refer to 23 - Body/Instrument Panel/CUPHOLDER, Instrument Panel - Removal) . |
| --- | --- |

| 4. | On vehicles with a close out panel, remove the screws (3) and remove the close out panel (2). |
| --- | --- |

| 5. | Remove the screws (2). |
| --- | --- |

| 6. | Using a trim stick C-4755 or equivalent, disengage the retainer clips that secure the instrument panel center bezel (1) to the instrument panel. |
| --- | --- |

| 7. | Disconnect the wire harness connectors (4) and remove the center bezel from the vehicle. |
| --- | --- |

.

| 1. | Disconnect and isolate the negative battery cable. |
| --- | --- |

| 2. | Remove the steering column opening cover. (Refer to 23 - Body/Instrument Panel/COVER, Steering Column Opening - Removal) |
| --- | --- |

| 4. | Remove the screws (2) that secure the top of the instrument cluster bezel (1) to the instrument panel. |
| --- | --- |

| 5. | Using a trim stick C-4755 or equivalent, disengage the two retainer clips that secure the top of the instrument cluster bezel to the instrument panel. |
| --- | --- |

| 6. | Carefully disengage the instrument cluster bezel from the instrument panel opening and remove the bezel. |
| --- | --- |

.

| 3. | Remove the four screws (2) that secure the instrument cluster (1) to the instrument panel structural support (3). |
| --- | --- |

| 4. | Pull the instrument cluster rearward far enough to access and disconnect the three instrument panel wire harness connectors (2) from the connector receptacles (1), C1, C3 and C4 from right to left on the back of the cluster housing. |
| --- | --- |

| 5. | Remove the instrument cluster from the instrument pane |
| --- | --- |