DOOR FINISHER


Removal and Installation


  FRONT DOOR

Zoom and Print Options

Removal
  1. Remove the power window switch assembly.
  -  Disconnect the harness connectors.
  2. Remove the cap from the inside door handle escutcheon and remove screw.
  3. Remove the pull handle cover.
  -  Remove the screws behind pull handle cover.
  4. Remove the seat memory switch.
  -  Disconnect the harness connector.
  5. Remove the step lamp.
  -  Disconnect the harness connector.
  6. Remove the door finisher and disconnect the lock cable and handle cable from the inside door handle assembly.   See: Front Door Panel > Removal and Replacement.
  7. Remove the inside door handle assembly.
  8. Remove door lock knob.

Zoom and Print Options

9. Remove the armrest screws (A), then remove the armrest (1).

  Installation
  Installation is in the reverse order of removal.

  REAR DOOR

Zoom and Print Options

Zoom and Print Options

Removal
  1. Remove the power window switch assembly.
  -  Disconnect the harness connector.
  2. Remove the pull handle cover.
  -  Remove the screws behind the pull handle cover.
  3. Remove the cap from the inside door handle escutcheon and the remove screw.
  4. Remove the inside door handle escutcheon.
  -  Remove the screw behind inside door handle escutcheon.
  5. Remove step lamp.
  -  Disconnect the step lamp harness connector.
  6. Remove the door finisher and disconnect lock cable and handle cable from inside door handle assembly.   See: Front Door Panel > Removal and Replacement.
  7. Remove the inside door handle assembly.
  8. Remove door lock knob.
  9. Remove the rear door tweeter.

Zoom and Print Options

10. Remove the armrest screws (A), then remove the armrest (1).

  Installation
  Installation is in the reverse order of removal.