A speed control servo is used only with the 4.7L V-8 engine.

The speed control servo assembly is attached to the bottom of the battery tray (1) .

| 1. | Disconnect negative battery cable at battery (both cables at both batteries if diesel). |
| --- | --- |

| 2. | To gain access to servo, remove plastic wheelhouse splash shield over left-front wheel. |
| --- | --- |

| 3. | Disconnect vacuum line (7) at servo . |
| --- | --- |

| 4. | Disconnect electrical connector (4) at servo . |
| --- | --- |

| 5. | Remove 3 servo mounting screws (5) . Depending on engine application, different sets of mounting lugs (2) are used to support servo to battery tray. While removing, note proper lugs. |
| --- | --- |

| 6. | Disconnect servo cable at throttle body. Refer to Servo Cable Removal/Installation. |
| --- | --- |

| 7. | Remove 2 mounting nuts (1) holding servo cable sleeve to bracket . |
| --- | --- |

| 8. | Pull speed control cable sleeve and servo away from servo mounting bracket to expose cable retaining clip (3) and remove clip. Note: The servo mounting bracket displayed is a typical bracket and may/may not be applicable to this model vehicle. |
| --- | --- |

| 9. | Remove servo (2) from mounting bracket. While removing, note orientation of servo to bracket |
| --- | --- |