### REMOVAL

WARNING: ON VEHICLES EQUIPPED WITH AIRBAGS, DISABLE THE SUPPLEMENTAL RESTRAINT SYSTEM BEFORE ATTEMPTING ANY STEERING WHEEL, STEERING COLUMN, DRIVER AIRBAG, PASSENGER AIRBAG, FRONT IMPACT SENSOR, SIDE IMPACT SENSOR, SIDE CURTAIN AIRBAG, OR INSTRUMENT PANEL COMPONENT DIAGNOSIS OR SERVICE. DISCONNECT AND ISOLATE THE BATTERY NEGATIVE (GROUND) CABLE, THEN WAIT TWO MINUTES FOR THE SYSTEM CAPACITOR TO DISCHARGE BEFORE PERFORMING FURTHER DIAGNOSIS OR SERVICE. THIS IS THE ONLY SURE WAY TO DISABLE THE SUPPLEMENTAL RESTRAINT SYSTEM. FAILURE TO TAKE THE PROPER PRECAUTIONS COULD RESULT IN ACCIDENTAL AIRBAG DEPLOYMENT AND POSSIBLE PERSONAL INJURY.

WARNING: WHEN REMOVING A DEPLOYED AIRBAG, RUBBER GLOVES, EYE PROTECTION, AND A LONG-SLEEVED SHIRT SHOULD BE WORN. THERE MAY BE DEPOSITS ON THE AIRBAG CUSHION AND OTHER INTERIOR SURFACES. IN LARGE DOSES, THESE DEPOSITS MAY CAUSE IRRITATION TO THE SKIN AND EYES.

- Disconnect the negative battery cable.

- Push in the adjustable steering column fully.

- Position the steering wheel so that the front wheels are in the straight-ahead position.

- Remove the ignition key and allow the steering to lock into position.

- Remove the airbag screws (1) on the steering wheel.

- Using a long hex tool (2), remove the tapered steering wheel bolt (1) while steadying the steering wheel.

- Carefully pass the connector from the airbag through the hole in the steering wheel.

- Remove the steering wheel from the vehicle.

- Check the horn/airbag and clock spring contacts for any damage. Replace if necessary.

.

- Remove the lower instrument panel cover (2).

- Remove the Instrument Cluster outer bezel (1).

NOTE: To ease the removal of the Instrument Cluster outer bezel, carefully pry the bezel from the top edge to disengage the retaining tabs from the Instrument Panel.

- Remove the retaining screws from Instrument Cluster.

- Rotate the Instrument Cluster away from the Instrument Panel.

- Disconnect the Instrument Cluster harness connectors from the back of the Instrument Cluster.

- Remove the Instrument Cluster from the vehicle.

.

- Disconnect the 2-pin CAN BUS harness connector (1) from the SKREEM module.

- Disconnect the 2-pin harness connector for the sentry key antenna ring.

- Disconnect the 18-pin harness connector (1) from the SKREEM module.

- Press the retaining tabs apart.

- Remove the SKREEM module from the base plate.

Reverse the procedure to install