### REMOVAL

- Release fuel pressure, refer to Fuel Pressure Release Procedure in this section.

- Disconnect negative battery cable.

- Remove fuel tank,

- Vacuum area before removing fuel pump module lock ring.

- Disconnect vapor line and electrical connector.

- Remove Fuel Pump Module lock ring.

NOTE: Use a brass punch to remove the 1/4 turn lock ring. Make contact only at the points shown

- Remove fuel pump module top.

- Drain Fuel Tank using an approved gasoline draining station.

- Disconnect electrical connector

- The wire connector to the passenger side level sensor needs to be disconnected before removing the reservoir from the tank.

- Tab location in fuel pump module for return line and fuel supply line

- Remove return line from pump module. Use a small screwdriver to pry tab back and tip hose to one side. Pry tab on other side back to release hose.

CAUTION: Care should be taken to not crack/break the locking tabs or supply line fitting.

- Remove fuel line from top of the pump module. Use a small screwdriver to pry tab back and tip hose to one side. Pry the tab on other side back to release hose.

- Tip fuel pump module on its side to remove fuel from reservoir.

- Remove fuel pump module.