STAR Case

Case Number 999922950 Vehicle Issue MIL on ¦ SAE P1391 TJ ¦ XJ ¦ ZJ => Check the distributor index;What is the general nature of your question or concern? >> Gasoline and Flex Fuel engine concerns What type of driveability concern is it? >> MIL on and/or PCM DTC's Have you checked TSB's & performed all applicable diagnostic procedures? >> YES * What PCM trouble code is present? (see note for HEX Code-to-PCode conversion)... >> P-1391, INTERMITTENT LOSS OR CMP OR CKP System or Component DTC / Error Message;Group 18 - Vehicle Performance / Driveability Recommendation Check for correct distributor index Check distributor and camshaft worm gear for damage (seized , bent, broken teeth, etc.). If ok, follow the MDS2 procedure: Manuals 14 Fuel and Ignition Ignition distributor removal and Installation Or follow procedure in the 8d secton of service manual