### RADIO C1 - 22 WAY

| CAV | CIRCUIT | FUNCTION |
| --- | --- | --- |
| 1 | A114 16GY/RD | FUSED B(+) (I.O.D.) |
| 2 | F306 18DB/PK | FUSED ACCESSORY RELAY OUTPUT |
| 3 | E14 20OR/TN | PANEL LAMPS DRIVER |
| 4 | - | - |
| 5 | - | - |
| 6 | - | - |
| 7 | X54 20GY (LOWLINE) | RIGHT FRONT SPEAKER (+) |
| 8 | X56 20GY/BR (LOWLINE) | RIGHT FRONT SPEAKER (-) |
| 9 | X55 20DG/BR (LOWLINE) | LEFT FRONT SPEAKER (-) |
| 10 | X53 20DG (LOWLINE) | LEFT FRONT SPEAKER (+) |
| 11 | Z514 16BK/LG | GROUND |
| 12 | A114 16GY/RD | FUSED B(+) (I.O.D.) |
| 13 | X60 20GY/YL (EXPORT) | RADIO 12 VOLT OUTPUT |
| 14 | D25 20WT/VT | PCI BUS |
| 15 | - | - |
| 16 | - | - |
| 17 | - | - |
| 18 | X51 22DG/DB | LEFT REAR SPEAKER (+) |
| 19 | X57 22DG/OR | LEFT REAR SPEAKER (-) |
| 20 | X58 22GY/OR | RIGHT REAR SPEAKER (-) |
| 21 | X52 22GY/DB | RIGHT REAR SPEAKER (+) |
| 22 | Z515 16BK | GROUND |