#### Heating and Air Conditioning/Controls/ACTUATOR, Blend Door/Removal

## REMOVAL

Labor Operations: Click to display a list of Labor Operations associated with this procedure

| WARNING: | On vehicles equipped with airbags, disable the airbag system before attempting any steering wheel, steering column, or instrument panel component diagnosis or service. Disconnect and isolate the negative battery (ground) cable, then wait two minutes for the airbag system capacitor to discharge before performing further diagnosis or service. This is the only sure way to disable the airbag system. Failure to take the proper precautions could result in accidental airbag deployment and possible personal injury or death. |
| --- | --- |

| NOTE: | The single zone heater-A/C system is equipped with a single blend door actuator. The dual zone system has two blend door actuators, one for the driver side blend-air door and one for the passenger side blend-air door. |
| --- | --- |

| NOTE: | LHD model shown in illustrations. RHD model similar. |
| --- | --- |

### SINGLE ZONE/DUAL ZONE DRIVER SIDE

| 1. | Disconnect and isolate the negative battery cable. |
| --- | --- |

| 2. | Remove the instrument panel silencer from the driver side of the instrument panel . |
| --- | --- |

| 3. | Remove the three screws (1) that secure the blend door actuator (2) to the driver side of the HVAC air distribution housing (3). |
| --- | --- |

| 4. | Remove the blend door actuator from the air distribution housing and disconnect the HVAC wire harness connector (4) and remove the actuator from the vehicle. |
| --- | --- |

### DUAL ZONE PASSENGER SIDE

| 1. | Disconnect and isolate the negative battery cable. |
| --- | --- |

| 2. | Remove the glove box from the instrument panel |
| --- | --- |

| 3. | Remove the three screws (1) that secure the blend door actuator (2) to the passenger side of the HVAC air distribution housing (3). |
| --- | --- |

| 4. | Remove the blend door actuator from the air distribution housing and disconnect the HVAC wire harness connector (4) and remove the actuator from the vehicle. |
| --- | --- |