#### 23 - Body / Convertible Top, CST and RHT Common Components / ASSEMBLY, Hydraulic, Motor and Pump/Removal

## REMOVAL

Labor Operations: Click to display a list of Labor Operations associated with this procedure

| NOTE: | The hydraulic system uses ARAL VITAMOL ZH-M fluid. When replacing components or topping off system due to leak, make sure to use only approved fluid. When adding fluid (Refer to 23 - Body/Convertible Top - Standard Procedure) . |
| --- | --- |

| 1. | Disconnect the battery negative remote cable. |
| --- | --- |

| 2. | Open decklid. |
| --- | --- |

| 3. | Remove the spare tire cover/floor panel. |
| --- | --- |

| 4. | Remove the rear trunk trim. |
| --- | --- |

| 5. | Remove the spare tire and jack. |
| --- | --- |

| 6. | Remove the two bolts (2) from the pump assembly. |
| --- | --- |

| 7. | Separate the pump from the bracket: a. Unwrap the insulation. b. Disconnect the electrical connector and un-clip the push pin. |
| --- | --- |

| OPEN COUNTER CLOCKWISE (CCW) DIRECTION (1) CLOSE CLOCKWISE (CW) DIRECTION (2) |
| --- |
| 8. | Release the pump pressure valve by turning it counter clockwise (1) two rotations. |

| 9. | Remove the bolts to the line retaining plate. |
| --- | --- |

| 10. | Move the lines and retaining plate out of the way. |
| --- | --- |

| 11. | Remove pump assembly from the vehicle. |
| --- | --- |

#### 23 - Body / Convertible Top, CST and RHT Common Components / ASSEMBLY, Hydraulic, Motor and Pump/Removal

## REMOVAL

Labor Operations: Click to display a list of Labor Operations associated with this procedure

| NOTE: | The hydraulic system uses ARAL VITAMOL ZH-M fluid. When replacing components or topping off system due to leak, make sure to use only approved fluid. When adding fluid (Refer to 23 - Body/Convertible Top - Standard Procedure) . |
| --- | --- |

| 1. | Disconnect the battery negative remote cable. |
| --- | --- |

| 2. | Open decklid. |
| --- | --- |

| 3. | Remove the spare tire cover/floor panel. |
| --- | --- |

| 4. | Remove the rear trunk trim. |
| --- | --- |

| 5. | Remove the spare tire and jack. |
| --- | --- |

| 6. | Remove the two bolts (2) from the pump assembly. |
| --- | --- |

| 7. | Separate the pump from the bracket: a. Unwrap the insulation. b. Disconnect the electrical connector and un-clip the push pin. |
| --- | --- |

| OPEN COUNTER CLOCKWISE (CCW) DIRECTION (1) CLOSE CLOCKWISE (CW) DIRECTION (2) |
| --- |
| 8. | Release the pump pressure valve by turning it counter clockwise (1) two rotations. |

| 9. | Remove the bolts to the line retaining plate. |
| --- | --- |

| 10. | Move the lines and retaining plate out of the way. |
| --- | --- |

| 11. | Remove pump assembly from the vehicle. |
| --- | --- |