#### 23 - Body/Convertible Top/ASSEMBLY, Hydraulic, Motor and Pump/Description

## DESCRIPTION

The power convertible top hydraulic system consists of:

- An electric hydraulic pump and motor (2)

- Hydraulic lines

- Two hydraulic cylinders (1)

- Wire harness assembly (3)

The hydraulic pump, motor, cylinders, lines and fluid are serviced only as an assembly. If a leak in the hydraulic system is found, the entire hydraulic pump/motor assembly must be replaced.

.

#### Body/Convertible Top/ASSEMBLY, Hydraulic, Motor and Pump/Removal

## REMOVAL

Labor Operations: Click to display a list of Labor Operations associated with this procedure

| 1. | Position the convertible top in the raised position. |
| --- | --- |

| 2. | Disconnect and isolate the negative battery cable. |
| --- | --- |

| 3. | Remove the rear seat cushion . |
| --- | --- |

| 4. | Remove the interior quarter trim panels |
| --- | --- |

| 5. | Remove the rear seat back |
| --- | --- |

| 6. | Remove the push-pins (1) that secure the convertible top well (2) to the rear seat back panel (3) and body (4) and remove the well liner. |
| --- | --- |

.

## INSTALLATION

Labor Operations: Click to display a list of Labor Operations associated with this procedure

| 1. | Position the hydraulic pump/motor assembly into the vehicle. |
| --- | --- |

| 2. | Install the hydraulic cylinders (1) onto the main pivot brackets. |
| --- | --- |

| 3. | Install the two bolts (1) that secure each hydraulic cylinder to the main pivot brackets. Tighten the bolts securely. |
| --- | --- |

| 4. | Align each rear seat back support bracket (2) to the previously marked bracket locations. |
| --- | --- |

| 5. | Install the three bolts and two nuts one at a time that secure each rear seat back support bracket. Make sure the position of the bracket aligns with each previously marked location. Tighten the fasteners securely. |
| --- | --- |

| 6. | Install the two nuts (1) that secure the hydraulic pump/motor assembly to the top of the shelf panel. Tighten the nuts securely. |
| --- | --- |

| 7. | Install the six retaining clips (3 per side) that secure the hydraulic hoses and wire harness to the body. |
| --- | --- |

| 8. | Connect the convertible top wire harness to the main body harness. |
| --- | --- |

| 9. | Install the protective cover (3) to the top of the hydraulic pump/motor assembly (4) located on the shelf panel (2). |
| --- | --- |

| 10. | Position the convertible top well liner (2) into the vehicle and install the push-pins (1) that secure the liner to the rear seat back panel (3) and body (4). |
| --- | --- |

| 11. | Install the rear seat back . |
| --- | --- |

| 12. | Install the interior quarter trim panels |
| --- | --- |

| 13. | Install the rear seat cushion. |
| --- | --- |

| 14. | Reconnect the negative battery cable. |
| --- | --- |

| 7. | Remove the protective cover (3) from the top of the hydraulic pump/motor assembly (4) located on the shelf panel (2). |
| --- | --- |

| 8. | Disconnect the convertible top wire harness from the main body harness. |
| --- | --- |

| 9. | Remove the two nuts (1) that secure the hydraulic pump/motor assembly to the top of the shelf panel. |
| --- | --- |

| 10. | Remove the six retaining clips (3 per side) that secure the hydraulic hoses and convertible top wire harness to the body. |
| --- | --- |

| NOTE: | Place a reference mark along the outer edge of the shelf seat brackets to ensure they are installed back to the original position. |
| --- | --- |

| 11. | Remove the three bolts and two nuts that secure each rear seat back support bracket (2) and remove both brackets. |
| --- | --- |

| 12. | Remove the two bolts (1) that secure each hydraulic cylinder to the main pivot brackets. |
| --- | --- |

| 13. | Remove each hydraulic cylinder (1) from the main pivot brackets and remove the hydraulic pump/motor assembly from the vehicle. |
| --- | --- |