Clearing a computer will erase everything, including anything that uses memory such as seats, mirrors, clocks, radio stations and computer values such as fuel trims and mode$06. The good part, is that it resets everything to zero, or a start over place that can remove any gremlins floating around. So here is the procedure to do this.

Remove both battery cables, negative first, then positive for (15) minutes and touch the (2) cable ends together for (10) seconds. When (15) minutes has lapsed, re-connect the cables to the battery, positive first, then negative. Now start the car and drive for 20 minutes with a lot of idling to see if the problem you were having is gone. Good luck to you.